# Windows 98 IR setup for ACT-IR2000B + IR2000L(or IR2000LC)

Caution: Do not install Infrared Driver Ver 3.0 under Windows98, it will not work at all.

Connect ACT-IR2000L adapter to the Mini DIN 8 IrDA port of IR2000B.  In PC BIOS, please disable COM2 (for IR2000B only).

- Go to “Control Panel” and double

click on “Add New Hardware”.

On the following screen, click on “Next” twice, then select “No, the device isn’t in the list”. And at the next screen, click on “Next”.

- Select “No I want to select

Hardware from the list”,

- Scroll down the menu and

highlight “Infrared Devices”,

then click on “Next” twice.

- Under “Manufacturers” Select

“(National Semiconductor)”,

and then in “Infrared Devices”

Select “(NSC-PC87108 Fast

Infrared Port)”.

Click on “OK”.

At “Infrared Transceiver A”, Select  “HP-HSDL-1100/2100”for IR2000L-PH,

IR2000LC-PH & IR2000L-HP*.

“Plug and Play”for IR2000L-PI,

IR2000LC-PI & IR2000L-IBM*.

Then click on “Next”.

At “Infrared Transceiver B”, Select

“None”. Then click on “Next”.

- At “ConfigIoBaseAddress”

Select “0x150”

Click on  “Next”.

- Follow the screen prompts until it asks you what default ports to use.  Select “Use default ports (recommended)”.  Click on “Next”.

When the process is completed, please go to “Control Panel” and double click on “Network”.  Select “NSC-PC87108 Fast Infrared Port”. Click on “Properties”.

In NSC-PC87108 Fast Infrared Port Properties Go to Resources and change I/O address range: 2E8-2EF,

IRQ: 3,

DMA: 0

Click “Close” and “OK”

- Please reboot your computer.

- Please refer to ACT-IR 210L/2000L/2000B User’s Manual, “Page 13” to continue installation.

- * Module type located on the shipping invoice.

(Ver.0.1, 9-03-98)