HDMI 0601 Switcher

1. Introduction

BHD-0610H is BeingHD exclusive premier video switcher that supports 6 HDMI inputs and 1 HDMI output. Easy to use with front button and RS232 for Switching, And have EDID automatic management to fit most displays.

- Features

1. Switch 6 inputs to 1 output display

2. Support resolution up to 4K2K

3. Equipped with EDID management capability

4. Power adaptor available to suit worldwide standards

5. Compatible with HDCP, EDID, Blu-ray DVD and HD audio output

3. Specification

| Input | HDMI x 6 |
| --- | --- |
| Output | HDMI x 1 |
| Resolution | Up to 4K2K |
| Power Supply | 100-240V, 50/60Hz |
| Connector Interface | HDMI |
| Standards | HDMI 1.4a |
| Pixel Clock | 340MHz |
| Operating Temperature | 0℃- 50℃ |
| Storage Temperature | -30℃- 70℃ |
| Weight | 300g |
| Dimension (WxHxD) | 370mm x 27mm x 94mm |

- Communication protocol

Baud rate: 115200

Data bits: 8

Stop bits: 1

Parity bit: None

1x1.  : Switch input 1 to the output

2x1.  : Switch input 2 to the output

3x1.  : Switch input 3 to the output

4x1.  : Switch input 4 to the output

5x1.  : Switch input 5 to the output

6x1.  : Switch input 6 to the output

- EDID Management setting

The setting map is on the back of the unit, please kindly check as below as well:

* D1, D2, D3, D4 stands for the number 1,2,3,4 at the front panel of the EDID

- Remote Control:

With this simple remote control, users only need to press the number keys from 1 to 6 to switch the inputs sources.

7. Packing list：

6x1 HDMI Switcher 1 unit,

Power code 1 pcs,

Remote control 1 pcs.