Integrator’s Guide

Congo

&

Rhine!

HD Component Video Matrix Switch

Digital Audio / Analog Audio Matrix Switch

Table of Contents

Table of Contents .............................................................................................................................................................................................. 2

Introduction ....................................................................................................................................................................................................... 3

Congo Features: .............................................................................................................................................3

Rhine Features: ..............................................................................................................................................3

Installation ......................................................................................................................................................................................................... 3

Unpacking ......................................................................................................................................................3

Front Panel Protective Film ............................................................................................................................4

Inputs .............................................................................................................................................................4

Outputs...........................................................................................................................................................4

RS-232 Serial .................................................................................................................................................4

USB ...............................................................................................................................................................4

Rear Panel IR .................................................................................................................................................4

Power .............................................................................................................................................................5

Rack Mounting (optional)...............................................................................................................................5

Operation ........................................................................................................................................................................................................... 6

Overview........................................................................................................................................................6

Using the front panel ......................................................................................................................................6

Controlling from an IR remote control............................................................................................................6

Last Command Feedback................................................................................................................................................................................ 7

Setup Menu ........................................................................................................................................................................................................ 7

Care and Maintenance ..................................................................................................................................................................................... 8

Restoring to Factory Defaults ......................................................................................................................................................................... 8

Specifications ..................................................................................................................................................................................................... 8

Performance ...................................................................................................................................................8

Power .............................................................................................................................................................9

Physical..........................................................................................................................................................9

2 Year Warranty............................................................................................................................................................................................. 10

2

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

Introduction

Congratulations on your selection of the Congo and/or Rhine audio/video matrix switches. The Congo is an

8x16 high definition component video matrix switch, and the Rhine is an 8x16 digital and analog video matrix

switch.

Both products are very similar in function, so this single user manual will guide you through both products.

Congo Features:

•	8 inputs of component video (YPbPr)

•	16 outputs of component video

•	High bandwidth video section (140 MHz) for 480i up to 1080p.

•	Attractive enclosure featuring brushed aluminum and high gloss acrylic front, with silver top cover.

•	Universal AC input power, 90-240VAC 50/60Hz with standard IEC320 receptacle.

•	All gold plated RCA connectors ensure a long life without corroded connectors.

Rhine Features:

•	8 inputs of digital audio (SPDIF), and 8 inputs of L+R analog audio

•	16 outputs of digital audio (SPDIF), and 8 inputs of L+R analog audio

•	Digital audio section is a wide band analog matrix that can easily handle composite video.

•	Independent routing of digital and analog audio

•	Attractive enclosure featuring brushed aluminum and high gloss acrylic front, with silver top cover.

•	Universal AC input power, 90-240VAC 50/60Hz with standard IEC320 receptacle.

•	All gold plated RCA connectors ensure a long life without corroded connectors.

Installation

The 8x16 Matrix Switch does not require ventilation, so it can have other equipment such as amplifiers stacked on top of it. The unit is also equipped with padded feet so it may be stacked on top of other equipment without causing damage. In either case, to avoid scratches, never slide equipment on top of one another.

Unpacking

The shipping carton for the 8x16 matrix switch will include the following items:

1 – Matrix Switch Unit

1 – AC Power cord

1 – 6’ USB cable

1- 6’ RS-232 cable

1 – User’s Guide

3

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

1 – CD-ROM driver disc

1 – Pair of rack mount ears with screws

If accessories were ordered, the carton may also contain:

1 – IR remote control

Front Panel Protective Film

There is a clear film over the front panel to protect it during manufacturing and shipping. Remove this film before using your  matrix switch.

Inputs

Connecting source devices to the matrix switch can be done in any order. All inputs have the same performance, so organize them as you see fit.

On the Congo, be sure to connect the green cable to the Y signal, as this is handled differently than the Pb and

Pr (blue and red) signals.

The Rhine’s connectors labeled “D” are intended for either SPDIF digital audio, or alternatively composite standard definition video. They can also be used for both signal type simultaneously, as long as care is taken not to route a signal of one type to a output of a different type. The analog audio matrix is labeled “L” and “R”.

Outputs

Having a true matrix switch allows you to treat each output as a ‘zone’. For example, Output 1 can be the home theater zone, and output 2 can be the master bedroom zone. In this case you would run a set of component video cables plus audio cables to each zone. The maximum length of cable to each zone will vary on the quality of the cable used, but if high quality cable is used, the 8x16 can support zones 300 feet away.

RS-232 Serial

The serial port on the rear panel is labeled “RS-232”. It is wired as a “DCE” device, which means it should be connected to a normal PCs RS-232 port with a straight through cable. Connection to most control systems should be with a straight through type serial cable, such as the cable provided with the matrix switch.

For the command protocols, please refer to the manual entitled “Integrator’s Guide to Serial Protocols”.

USB

If you plan to use the USB communication feature of the matrix switch, connect the USB cable to the PC’s USB

port (flat end), and the other end (square end) to the matrix switch.

Optionally you may choose to connect this cable later when you are prepared to install the driver CD-ROM. Connecting the cable will activate MS Windows plug and play wizard. On disconnect and reboots, MS Windows will remember what COM port this device was assigned.

Rear Panel IR

The rear panel connector labeled “IR” is for direct connection to a control system. It is a 3.5mm 2 pin jack, and accepts un-modulated IR. It is polarity insensitive, however normally the ‘tip’ is the active signal, and the

‘sleeve’ is the ground.

4

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

Note: Some IR repeater systems are designed to work only with their own IR blasters. Many integrators will cut these blaster cables and add a 3.5mm plug on the end. In some cases this will work fine, however some low end IR repeater systems will have too much noise in their signal, and can prevent signals from being properly decoded. Your results may vary.

Power

Once all the input and output connectors are in place, connect the supplied power cable to the AC input. If you are not in North America, you may use your own standard IEC320 power cable with the matrix switch. The power supply will detect whatever voltage is supplied (from 90V to 240V AC, 50-60Hz), and adjust accordingly.

Rack Mounting (optional)

The product ships with the rack mount ears detached from the unit. This is to prevent damage to the chassis during shipment. Use the supplied screws to attach the ears. The rack ears are universal, so they fit on either side.

The chassis is a 2 rack units high only when the bottom feet are removed. Removal requires a Philips screwdriver. Be careful when turning over the unit as to not scratch the top paint

5

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

Operation

Overview

The Congo and Rhine are designed to be controlled form a third party control system, either via RS232 or IR. The buttons on the front panel allow the control of power and status feedback, however matrix control must be performed from external sources.

Using the front panel

The 8x16 matrix switch’s front panel uses TouchSense! technology. This is different from many other front panels you have seen with ‘membrane’ or ‘dome’ type buttons. The TouchSense!  panel senses a human finger touching the acrylic panel without any moving parts. For you, the user, this means that you need not press hard to activate a button, a light tap will do.

Powering the 8x16 matrix switch on and off is accomplished by pressing the power button. To prevent accidental power offs, two button presses are required to shut down the matrix.

In the normal powered on mode, the Congo and Rhine will display the last command received. This is helpful for troubleshooting your control sequences. If the last command attempted was not received properly or was not formatted correctly, it will not appear on the display.

You can also use the left/ right arrow keys and the select button to access the setup menu. The setup options will be discussed in the next section. Generally when you are presented with a choice on the display, pressing select will toggle through the choices. Changes in the matrix switch performance or features takes place right away, so changes do not need to be saved manually.

Controlling from an IR remote control

Controlling the matrix switch using IR follows the basic sequence of:

#, Out, # # – Standard sequence for switching (both Congo and Rhine). Note that the output number is always two digits, so output 1 is represented by “01”

On the Congo, starting the sequence with the “In” command is the only option, since there is only one level to the matrix

On the Rhine, starting with the “In” command control both digital and analog audio levels of the matrix. The digital audio matrix level can also be controlled independently by the following:

Audio1, #, Out, # # – Controls digital audio matrix (Rhine)

Likewise, the analog audio matrix level can be controlled independently by the following:

Audio2, #, Out, # # – Controls analog audio matrix (Rhine)

Party Mode Shortcut:

To route a single input program to all outputs, also known as party mode, use the select key followed by the desired input:

Select, # Sends input # to all outputs

6

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

Last Command Feedback

The normal display shown on the front panel display can be changed to the command feedback screen. This screen will display the last received command, and is very helpful during control system programming and debugging.

To access this screen, use the the < (left arrow) or > (right arrow) buttons either on the front panel or the IR

remote until the Last Command screen is displayed.

Setup Menu

The user setup menu is only accessible with an IR remote, not from the front panel. The same settings can also be controlled from the serial ports. Refer to the Serial Protocols document for more information on the commands.

To start the setup menu, press “Setup” on the remote control.

Use the  < (left arrow) and  > (right arrow) buttons to navigate through the different options. Use the “Select” button to change any of the optional settings.

The menus are as follows:

Setup:Panel LEDs

This option will turn off all the front panel LED lights. The matrix’s behavior is otherwise unchanged. The default in ON

Setup:Disp Lamp

This option will set the display brightness to one of four levels. The default is 100%

Setup:AC Pwr

This option control what the matrix will do when AC power is first applied, or after a power outage. Selecting “ON” (default) will force the unit to turn on, and the previous switch state will be restored. Selecting “Stby” will cause the unit to enter standby mode.

Setup:Touchpanel

This option will disable the front panel buttons. The default in ON

Setup:TouchSense

Setup:TouchDelay

These two options work together to control the front panel touch button performance. The TouchSense setting controls the overall sensitivity, while the TouchDelay setting controls the detection delay, similar to a

‘debounce’ function.

If the buttons are falsely triggered by outside interference, setting the TouchSense to “LOW” and the

TouchDelay to “HIGH” will likely remedy the situation.

7

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

If the buttons are difficult to press with smaller fingers, setting the TouchSense to “HIGH” will improve the sensitivity. Setting the TouchDelay to “LOW” will not change the sensitivity, but will make the button response seem faster.

Any of the above selections will be applied instantly. There is no need to save the changes. At any time the user may press exit to return to the home screen, or wait 10 seconds and the home screen will return on it’s own.

Care and Maintenance

The 8x16 matrix switch does not require any regular maintenance besides keeping it clean.

Never use harsh cleaners or solvents on the 8x16 front panel. There are several dusting products for electronics, and standard glass cleaner may be used.

Spray any liquids onto a towel first, then wipe the front of the 8x16 with the moist towel.

Should the 8x16 matrix switch fail to operate as expected, please contact HDTVSupply.com for service advice. THERE ARE NO ADJUSTMENTS OR USER SERVICEABLE PARTS INSIDE THE CABINET.

Restoring to Factory Defaults

Just in case you should disable the front panel or IR input via the USB or RS-232 port, you may require a way to restore those features without using the ports again. To restore the 8x16 matrix switch back to factory settings, do the following:

! Unplug the unit for 10 seconds, then plug it back in. The 8x16 should be in standby mode.

! On the front panel, slowly press 0, 0, 7.

The unit will then enter Initialization, and when complete, return to standby mode. The front panel and IR will work as normal.

Specifications

Performance

Component Video (Congo)

Input coupling 		AC Input impedance/termination 	75 ohms

Output coupling 	DC

Output impedance 	75 ohms source terminated

Output video bandwidth (-3dB) 	140 MHz

Crosstalk 	Below –80dB

Video modes 	480i, 480p, 540i, 540p, 576i, 576p,

720p, 1080i, 1080p

Video vertical rates 	24, 25, 29.97, 30, 50, 59.97, 60

Digital Audio (Rhine)

Output bandwidth (-1dB) 	10 MHz

Crosstalk 	Below –80dB

8

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

Analog Audio

Input termination 	10K ohms

Audio bandwidth 	DC-100KHz, +/- 0.5dB

Gain and output type 	Unity gain, low impedance output

Power

Input voltage 	90-240V AC 50-60Hz  autosensing

Input power (Congo) 	 5W “On”, 2W “standby” Input power (Rhine) 	12W “On”, 6W “standby”

Dimensions

Dim. with feet (removable)

Physical

17”W x 3.5”H x 10.75”D

17”W x 3.75”H x 10.75”D

Unit Weight 	8.8 lbs (typical) Shipping weight 		13 lbs (typical)

9

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)

3 Year Warranty

HDTVSupply.com warrants this product against defects in material and workmanship for a period of 3 years. This warranty applies to the original end-user purchaser and installation service provider. HDTVSupply.com will, solely at its option, repair or replace this product with a functionally equivalent new or factory- reconditioned product during the warranty period. The consumer should contact the installation service provider that resold the product who will in turn deliver the product to HDTVSupply.com. All transportation risks and costs in connection with this warranty service are the responsibility of the consumer.

In order to keep this warranty in effect, the product must have been handled and used as prescribed in the instructions accompanying this warranty. This warranty does not cover any damage due to accident, misuse, abuse, or negligence. Repair or replacement, as provided under this warranty, is your exclusive remedy. HDTVSupply.com shall not be liable for any incidental or consequential damages. Implied warranties of merchantability and fitness for a particular purpose on this product are limited to the duration of this warranty.

Some states/countries do not allow the exclusion or limitation of incidental or consequential damages, so the above limitation or exclusion may not apply to you. Some states/countries do not allow limitations on how long an implied warranty lasts, so the above limitation may not apply to you. This warranty gives you specific legal rights, and you may also have other rights that vary from state to state and country to country.

© 2010

HDTVSupply.com www.HDTVSupply.com

10

8x16 Matrix Switch User’s Guide (DOC42-00018-A_Congo&Rhine.doc)