USER MANUAL

Table of Contents

1.0 Introduction.......................................................................01

2.0 Feature...............................................................................01

3.0 Specification......................................................................02

4.0 Package Content................................................................02

5.0 Panel Description...............................................................03

6.0 Connection and Operation................................................03

AHD/CVI/TVI 1x2 Splitter

Dear Customer

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

- Introduction

This AHD/CVI/TVI splitter enables you to distribute a single CVBS signal to two monitors simultaneously. It features built-in amplifier to amplify the signal to achieve long cable runs, up to 300-500meters. It also features built-in filter for signal processing to eliminate signal interference. For added benefit, the splitter comes with ESD protection, not only offer human body mode or device level, but also to address system-level risks.

2.0 Feature

* AHD/CVI/TVI input supported resolution:

720p@25/30Hz ,720p@50/60Hz, 1080p@25/30Hz

* Support AHD/CVI/TVI signal transmission distance up to 300-500m

* Coaxial cable impedance: 75Ω

* No need to install drivers, portable, flexible, plug and play.

* Support ESD protection on all signal pins

3.0 Specification

| Input Signal | 1x AHD/CVI/TVI Signal |
| --- | --- |
| Output Signal | 2x AHD/CVI/TVI Signal |
| AHD/CVI/TVI Input Resolution | 720p@25/30Hz ,720p@50/60Hz, 1080p@25/30Hz |
| AHD/CVI/TVI Output Resolution | 720p@25/30Hz ,720p@50/60Hz, 1080p@25/30Hz |
| Limited Warranty | 1Year Parts and Labor |
| Operating Temperature | 0℃ to 40℃ |
| Operating Humidity | 10% to 85 % RH (no condensation) |
| Storage Temperature | -10℃ to +80℃ |
| Storage Humidity | 5% to 90% RH (no condensation) |
| Power Supply | 12V DC@1A |
| Power Consumption(Max) | 1W |
| Splitter Unit Cert | FCC.CE, RoHS |
| Power Supply Cert | CE,FCC, RoHS |
| User Manual | English Version |

Note: Specification is subject to change without notice.

Cable quality affects transmission distance and product performance.

- Package Content

1) Main Unit

2) Power Adapter 12V@1A

3) User Manual

5.0 Panel Description

6.0 Connection and Operation

(1) Connect the product to appropriate power;

(2) Connect the AHD/CVI/TVI signal to “IN” through 75Ω coaxial cable (recommend BELDEN 1694 A cable or of same quality cable）

(3) Connect AHD/CVI/TVI monitors（ or other AHD/CVI/TVI devices）to “OUT1”(“OUT2”) interface through 75Ω coaxial cable.

6.1 Connection Diagram