USER MANUAL

Table of Contents

1.0 Introduction........................................................................01

2.0 Features...............................................................................01

3.0 Specifications......................................................................02

4.0 Package Contents................................................................02

5.0 Panel Descriptions...............................................................03

6.0 Connection and Operation................................................03

SDI 1X2 Splitter

Dear Customer

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Phase keep this manual for future reference

1.0 Introduction

This 1x2 SDI splitter distributes one SDI signal to 2 simultaneous SDI outputs. It supports full range of SDI signal formats including 3G-SDI, HD-SDI, SD-SDI with easy operation and high reliability. Using broadcast quality processing technology, it delivers high definition, lossless and lag-free distribution. This splitter can be widely used in SDI broadcast room, no-linear editing field, CCTV security system and training showroom etc.

2.0 Features

* Features equalizer circuit on the input and outputs, allowing it to support long cable runs

* Support multiple video resolution：

• SD 525i and 625i

• HD 720p@24, 25, 30, 50 and 60 Hz

• HD 1080i@50, 60 Hz

• HD 1080p@24, 25, 30, 50 and 60 Hz

* Support multiple color space：

• RGB or YCbCr 4:4:4 sampled

• YCbCr 4:2:2 or 4:2:0 sampled

* Support wide range of data rates：270Mbps～2.97Gbps.

* Support multiple deep color:8bit、10bit、12bit.

3.0 Specifications

| Input Connector | 1x SDI BNC Male |
| --- | --- |
| Output Connector | 2x SDI BNC Male |
| Supported Cable Length (BELDEN 1694A) | 3G Mode: up to 100m |
|  | HD Mode: up to 200m |
|  | SD Mode: up to 400m |
| Limited Warranty | 1Year Parts and Labor |
| Operating Temperature | 0℃ to 70℃ |
| Operating Humidity | 10% to 85 % RH (no condensation) |
| Storage Temperature | -10℃ to +80℃ |
| Storage Humidity | 5% to 90% RH (no condensation) |
| Power Supply | 5V DC@2A |
| Power consumption(MAX) | 1.2W |
| Splitter Unit Cert | FCC.CE, RoHS |
| Power Supply Cert | CE,FCC, RoHS |
| User Manual | English Version |

Note: Specifications are subject to change without notice.

4.0 Package Contents

1) Main unit

2) Power adapter 5V@2A

3) User Manual

5.0 Panel Descriptions

6.0 Connection and Operation

6.1 Connection

(1) Connect the product to appropriate power;

(2) Connect the SDI signal to “IN” through 75Ω coaxial cable of high quality（BELDEN 1694 A cable or equivalents as well）

(3) Connect SDI monitors（ or other SDI devices）to “OUT1”（ “OUT2”） interface through 75Ω coaxial cable.

6.2 Connection Diagram