USER MANUAL

Table of Contents

1.0 Introduction......................................................................01

2.0 Feature............................................................................01

3.0 Specification.........................................................................02

4.0 Package Content.............................................................02

5.0 Panel Description............................................................03

6.0 Connection and Operation..............................................03

AHD TM to HDMI TM +AHD TM Converter Scaler (720P/1080P)

Dear Customer

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

- Introduction

This converter can convert AHD TM signal (Analog High Definition) to HDMI TM signal with AHD TM loop out. The device comes with a upscaler that will allow you to adjust the output signal to a resolution (720p/1080p) that is compatible with your HDMI TM -enabled display. To ensure you maintain perfect high-definition video quality, the AHD TM -HDMI TM converter features supports resolutions up to 1080p, allowing you to convert AHD TM to HDMI TM without sacrificing video quality .For hassle-free installation, the AHD TM to HDMI TM converter offers a plug-and-play solution and requires no software or driver installation.

- Feature

* Input: 1x AHD

* Output: 1 x AHD; 1 x HDMI;

* AHD input supported resolution: 720p@25Hz/30Hz,720p@50Hz/60Hz,1080p@25Hz/30Hz

* Built-in scaler allows user to adjust the output signal to 720p@60Hz or 1080p@60Hz

* Support OSD (On-Screen Display) for input and output resolutions

* No need to install drivers, portable, flexible, plug and play.

* Coaxial cable impedance: 75Ω

* Support AHD loop out

* Two Outputs could be displayed simultaneously.

* Support wide range voltage for power adapter:5V~12V

3.0 Specification

| Input Signal | AHD Signal |
| --- | --- |
| Output Signal | HDMI signal x1,AHD signal x1 |
| AHD Input Resolution | 720p@25Hz/30Hz,720p@50Hz/60Hz,1080p@25Hz/30Hz |
| AHD Output Resolution | 720p@25Hz/30Hz,720p@50Hz/60Hz,1080p@25Hz/30Hz |
| HDMI Output Resolution | 720p@60Hz/1080p@60Hz |
| Limited Warranty | 1 Year Parts and Labor |
| Operating Temperature | -40℃ to +120℃ |
| Operating Humidity | 10% to 85 % RH (no condensation) |
| Storage Temperature | -30℃ to +50℃ |
| Storage Humidity | 5% to 90 % RH (no condensation) |
| Power Supply | 5V~12V DC |
| Power Consumption (Max) | 5W |
| Converter Unit Cert. | FCC,CE, RoHS |
| User Manual | English Version |

Note: Specification is subject to change without notice.

4.0 Package Content

1) Main Unit

2) 5V DC Power Adapter

3) User Manual

5.0 Panel Description

6.0 Connection and Operation

Connection

A. connect the input device with the converter over standard Coaxial cable

B. connect the HDMI display with the converter over standard HDMI Cable

C. connect the AHD display with the converter over standard Coaxial cable

D. Power on all devices