USER MANUAL

Table of Contents

1.0 Introduction……………………………………………… 1

2.0 Feature…………………………………….……..……….1

3.0 Specification………………………………….……..……2

4.0 Package Content…………………………………….….. 2

5.0 Panel Description……………………………….…….… 3

6.0 Connection and Operation……………. .………….….… 3

SDI to AV+SDI Scaler Converter 3G/HD/SD-SDI

Dear Customer

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

- Introduction

The SDI to AV converter enables you to turn a 3G/SD/HD-SDI video signal into an AV video output and an SDI display. The device comes with a scaler that will allow you to adjust the output signal to a resolution (480i/576i) that is compatible with your legacy A/V display. The converter also features an SDI loop out for distributing the SDI signal at 300m away for SDI-SDI signal, 200m way for HD-SDI signal and 100m for 3G-SDI signal.

2.0 Feature

*Support date transfer rate 2.970Gbps, 2.970/1.001Gbps, 1.485Gbps, 1.485/1.001Gbps and 270Mbps

*Support equalization and signal re-clocked loop out

*Support auto video mode detection for 3G/HD/SD-SDI signal

*Simultaneous display for SDI and AV signals

*Support LPCM 2.0 channel audio

*Support signal transmission distances up to 300M for SD-SDI signal, 200M for HD-SDI signal and 100M for 3G-SDI signal

Note: Distance tested via standard Belden 1694A cable. Operating distances may vary for cable with different specs.

3.0 Specification

| Input Signal | SDI Signal (HD-SDI, SD-SDI and 3G-SDI) |
| --- | --- |
| Output CVBS Signal | PAL/NTSC |
| SDI Data Transmission Rate | 2.970 Gbps and 2.970/1.001 Gbps, 1.485Gbps, 1.485/1.001Gbps and 270Mbps |
| SDI In/Out Resolution | SD-SDI:480i@60Hz,576i@50Hz HD-SDI:720p@50/60Hz,1080i@50/60Hz 3G-SDI:1080p@24/25/29.97/30/50/59.94/60Hz |
| Limited Warranty | 1 Year Parts and Labor |
| Operating Temperature | 0℃ to +50℃ |
| Operating Humidity | 10% to 85 % RH (no condensation) |
| Storage Temperature | -10℃ to +80℃ |
| Storage Humidity | 5% to 90 % RH (no condensation) |
| Power Supply | 5V DC |
| Power Consumption (Max) | 5W |
| Converter Unit Cert. | FCC,CE,RoHS |
| User Manual | English Version |

Note: Specification is subject to change without prior notice.

4.0 Package Content

1) Main Unit

2) 5V DC Power Supply

3) User Manual

5.0 Panel Description

6.0 Connection and Operation