HOW TO CONNECT AN IPAD/IPHONE TO A COLORADO MATRIX SWITCH

This iPad & iPhone App provides a free fully customizable control package for all of our Colorado matrix switchers. It can run on any IOS platform and can connect using many common options. It is primarily targeted for commercial applications in order to provide an easy to use control solution.

The iPad & iPhone App can also be used as a debug tool during installation, a supplemental control method to an IR based system, or a primary residential control system in cost sensitive applications.

After buying the iPad/iPhone app go to http://www.hdtvsupply.com/colorado-ipad-ap.html and read and Print Out all the TABs.

The app is at the Aps section of the ITunes store. Search for VSXCtl and install them in both your iPhone and iPad, if you have both. It is free.

Colorado using Ethernet to serial adapter:

The unit works on a WIFI network. The full path of the wiring would be iPad/iPhone =>WIFI => wireless router => wired Ethernet => ETHERNET to RS232 adapter => Supplied RS232 cable => Colorado.

- Connect to the Ethernet to serial adapter  using the included female => female RS232 cable (and a USB=>rs232 adapter if needed)

- Switch the Ethernet to serial adapter to "console"

- Using a serial terminal program such as the below hyper-terminal program, setup the desired static IP address of the adapter (default login is user=root, password=root)

- All other default settings are OK so SAVE and EXIT

- Connect the Ethernet to serial adapter serial port to the Colorado Control female port using the female => male RS232 cable

- Switch the Ethernet to serial adapter from "Console" to "Data"

- Set the IP address to the static IP of the adapter

- Set the port number to port number of the adapter (6001 is default)

- User name, password are not used

- Set use RFC2217 to OFF (Used in our first version only)

- Set the 16V & 16A2 mode to OFF unless you have a video and audio switch installed

- Remember to hit the "return" button/key after you have entered the IP address on the iPad.  If you don't it will not save the value and will always use the default IP address.

Configuration instructions:

- Set the IP address to the static IP address of the Ethernet to serial adapter

- Set the port number to 23

- User name and password are not used

- Set use RFC2217 to OFF (Used in our first version only)

- Set 16V & 16A2 mode to OFF unless you have both switches installed

- Remember to hit the "return" button/key after you have entered the IP address on the iPad.  If you don't it will not save the value and will always use the default IP address.

If you are updated the iPhone app please power cycle the Ethernet to serial adapter.

Here is the program to setup the IP address…http://www.hilgraeve.com/hyperterminal/

For a video on the setup see the MORE VIDEOS Tab at

http://www.hdtvsupply.com/colorado-ipad-ap.html

HDTV Supply, Inc.
3835-R East Thousand Oaks Blvd
Unit 295
Westlake Village, CA 91362
(800) 841-9238
(805) 277-1870 Direct

TECH Support: support@hdtvsupply.com