IR Extender Kit

The IR Extender Kit includes 1 Target (labeled RX), 1 Emitter (labeled TX) and an HDMI adapter. The kit can be used with any of our HDMI devices that state has the IR Extender kit on the product page as an option.

HDMI Matrix: When you use the IR Extender Kit with an HDMI Matrix you connect the emitter (TX) to the 3.5mm jack on the matrix labeled IR Ext. The target (RX) connects to the HDMI adapter that is plugged into the rear of a television. This allows the user to control the devices in the equipment closet from the TV location.

The Matrix also supports reverse path IR. A target (RX) is connected to one of the two 3.5mm jacks on the matrix labeled Backward IR Channels. The Emitter (TX) connects to an HDMI adapter plugged into the rear of a television and is aimed at the IR window on the TV. This allows the user to change channels on a TV from inside the equipment closet.

The IR Window on the Matrix is used with the included IR control to switch inputs and outputs on the matrix.

HDMI Splitter:  When you use the IR Extender Kit with an HDMI Splitter you connect the emitter (TX) to the 3.5mm jack on the splitter labeled IR. The target (RX) connects to the HDMI adapter that is plugged into the rear of a television. This allows the user to control the devices in the equipment closet from the TV location.

HDMI Switcher:  When you use the IR Extender Kit with an HDMI Switch you connect the emitter (TX) to the 3.5mm jack on the matrix labeled IR Ext. The target (RX) connects to the HDMI adapter that is plugged into the rear of a television. This allows the user to control the devices in the equipment closet from the TV location.

The Splitter also supports reverse path IR. A target (RX) is connected to the 3.5mm jack on the matrix labeled IR.  The Emitter (TX) connects to an HDMI adapter plugged into the rear of a television and is aimed at the IR window on the TV. This allows the user to change channels on a TV from inside the equipment closet.

CEC / IR Switch: CEC "Connected Equipment Control" is an HDMI feature specification that allows one device to control multiple. For example, when you pick up the Blu‐ray DVD remote and turn on the unit, the TV turns on and sets itself to the correct HDMI input while the AV receiver turns on and sets itself to the correct HDMI input. Unfortunately this is not a global spec and each manufacturer's use changes so it only works with single brands of equipment.

If the user has CEC turned on with all of their equipment, the user sets the CEC / IR switch to CEC. If the user does not have CEC turned on with their equipment, set the switch to IR. The user will almost always have the switch set to IR.

HDTV Supply, Inc.
3835-R East Thousand Oaks Blvd, Unit 295
Westlake Village, CA 91362
(800) 841-9238
(805) 277-1870 Direct
(805) 371-4070 FAX - General
(805) 435-2623 FAX for orders, RMA info and availability
WEB: www.HDTVSupply.com
EMAIL: support@hdtvsupply.com
MOBILE FRIENDLY: Mobile Friendly page or http://m.hdtvsupply.com