GasAlertMicro

H2S, CO, O2 , SO2, Combustibles

Multi-Gas Detector

s

Protect Yourself

Compact (2.4 x 4.0 x 1.3 in / 6 x 10 x 3.3 cm) and lightweight (7.4 oz. / 211 g)

Integral concussion-proof boot for the most rugged environments 
Continuous LCD shows simultaneous gas concentrations for 
H2S, CO, O2, SO2, combustibles (0-100% LEL or 0-5.0% Methane) 
Powered by two AA alkaline or NiMH cells  (run-time typically 
16-18 hours)

Provides 95 dB alarm tone and two bright wide-angled alarm bars Equipped with internal vibrating alarm for high noise areas

Backlight: low light (auto); in alarm (auto); and on demand reactivation

Four alarm levels: Instant Low and High Alarm for all gases; TWA (time weighted average) and STEL (short term exposure limit) for H2S, CO, SO2; OL (over limit alarm) for 
combustible gases

Simple automatic calibration procedure; compatible with BW MicroDock II Automatic Test and Calibration System

Records TWA, STEL and maximum exposures to gas and displays readings on command

User selectable fi eld options include: confi dence beep, pass code protection, latching alarm, calibration due date, bump due date, “SAFE” display function, language, span concentration values, combustible sensor measurement selection (0-100%LEL or 
0-5.0% v/v methane) and stealth mode

Full function self-test of: sensor, battery and circuitry integrity; and audible/visual alarms

Delivered ready for use with sensors, two AA alkaline cells, stainless steel alligator belt clip, calibration hose/cap and 
instructions

BAM

Optional Charger Kits

GA MicroBatt rechargeable battery

and slip-in charger cradle.

The GasAlertMicro can be recharged while the

battery pack is installed, or the pack can be

removed for separate recharging.

GasAlertMicro Charger II

Ordering Information

GAMIC-4 	H2S, CO, O2, LEL 	GAMIC-3M 	CO, O2, LEL

GAMIC-3H   H2S, O2, LEL 	GAMIC-3S 	SO2, O2, LEL

GAMIC-2 	O2, LEL 	GAMIC-2HW  H2S, LEL

With User-Downloadable Datalogger

Includes 32 MB Flash MultiMediaCard and software.

Add suffi x “-DL2-IR” for detector equipped with datalogger.

With Charger Kit

Includes detector, standard accessories plus charger and battery pack. 
GAMIC-4-E3 	with 4-gas detector and GA MicroBatt charger kit

GAMIC-4-E5 	with 4-gas detector and GasAlertMicro Charger II

GasAlertMicro SamplerPak

Includes detector, standard accessories plus the Sampler (external motorized sampling pump), sampling hoses, sampling tubes and a carrying case.

GAMIC-4-SK 	with 4-gas detector

GAMIC-4-SKC 	with 4-gas detector and charger kit

Value Added Confi ned Space Kits

Kits include detector, standard accessories plus a hard-sided carrying case, 3 m/10 ft. sampling hose, 4-port charger, 4 NiMH batteries, 34 liter calibration gas cylinder with regulator.

With The Sampler motorized sampling pump

GAMIC-4-CK-IR-SP    with 4-gas detector

GAMIC-4-CK2-IR-SP   with 4-gas datalogging detector

Contact BW for available accessories

www.gasmonitors.com

Email: info@bwtnet.com

SPECIFICATIONS

GasAlertMicro

H2S, CO, O2 , SO2, Combustibles Multi-Gas Detector

Gas: 	H2S 	CO 	O2 (% by vol.) 	SO2

Measuring Range: 	0-100 ppm 	0-500 ppm 	0-25.0% 	0-100 ppm

DETECTOR: 	1, 2, 3 or 4-gas detector

Auto zero: 	Yes

Calibration: 	Automatic

Combustibles (Field Select)

0-100 % LEL or

0-5% by vol. methane

Offering a large array of feautrues,

the ultra-compact and durable

GasAlertMicro has set new

standards in the multi-gas detection-
at an economical price.

Simultaneously displaying H2S,

CO, O2, SO2, or combustibles,

GasAlertMicro is suited to a wide

range of applications, including

HAZMAT response, confi ned space 
entry and post-inspection fi re safety.

Field-selectable user options allow

GasAlertMicro to be customized to virtually any environment. Calibration due dates and alarm settings can

be confi gured to meet specifi c

industry requirements, and the

pass code protect function ensures 
tamper-proof operation by preventing 
unauthorized users from accessing

calibration options.

In a world of multi-gas detectors,

GasAlertMicro truly is more for less.

s

For further information:

1-888-749-8878 	USA

1-800-663-4164 	Canada

+44 (0) 1869 233004 Europe

+971-4-8871766 	Middle East

+61-438-887-232 	Australia

+852-2974-1783 	China

+65-6465-4151 	South East Asia

+1-403-248-9226 	Other Countries

Corporate Headquarters

2840 - 2 Avenue S.E.

Calgary, AB, Canada  T2A 7X9

Phone: +1-403-248-9226

Backlight: 	Low light (auto); alarm condition (auto); reactivation on demand

Full function self-test: 	Sensor integrity, circuitry and battery; audible/visual alarms

Sensor:    Plug in, electrochemical cell (toxic and oxygen); Plug in, catalytic (LEL)

User fi eld options: 	Confi dence beep, pass code protection, latching alarms, calibration due date,

bump due date, “SAFE” display function, language selection, span concentration

values, combustible sensor measurement selection (0-100%LEL or 0-5.0% v/v

methane), enable/disable automatic O2 calibration, STEL calculation period,

disable backlight, battery type and stealth mode.

Datalogging models only: clock, calendar and sampling rate

ALARM INDICATORS:    Clearly advises alarm levels both visually and audibly

Visual alarms: 	Two fl ashing alarm bars visible from all angles

LCD indicates gas present and alarm levels encountered

Audible alarm: 	95 dB variable pulsed audible alarm at 1 ft. / 30 cm (typical)

Vibrator alarm: 	Pulses warning in gas alarm conditions, or for any status alarms

Other: 	Low battery, over range, multiple gas and missing sensor

ALARM LEVELS:   Instantaneous Low Alarm for all gases; instantaneous High Alarm for all gases;

TWA (time weighted average) and STEL (short term exposure limit) for H2S, CO,

SO2; OL (over limit alarm) for combustible gases

LCD:   Continuous, alphanumeric gas readout and status display advises:

Gases monitored:    H2S, CO, O2, SO2, combustibles (0-100% LEL or 0-5.0% methane)

Gas concentration: 	Simultaneous and continuously displays gas concentration(s) present

(in ppm, %LEL, or % v/v)

TWA ppm or %:   Records STEL and TWA exposures and displays on demand

Peak ppm or %:   Records and displays peak exposure to gas and displays on demand

Alarm setpoints: 	Displayed on activation

TESTS:

Full function self-test: 	Full function self-test on activation

Battery: 	Continuous

GENERAL SPECIFICATIONS:   Rugged, composite material with integral concussion-proof boot 
	Operating temperature: 	-4 to 122 oF / -20 to 50 oC

Temperature code:    T4 with GA MicroBatt battery pack

Humidity: 	5% to 95% RH (non-condensing)

EMI/RFI:    Complies with EMC Directive 89/336/EEC

Ingress Protection: 	IP65

Battery run-time: 	16-18 hours on two AA alkaline cells (typical)

14-16 hours on two NiMH rechargeable cells (typical)

Size: 	2.4 x 4 x 1.3 in. / 6 x 10 x 3.3 cm

Weight: 	7.4 oz. / 211 g

WARRANTY:   Full 2 year warranty including all sensors

DATALOGGER OPTIONS:   User-downloadable datalogger

Data recorder: 	All events and occurrences

Sampling rate: 	Factory set at 5-second intervals and user-settable from

1 to 127-second intervals

Storage: 	4.4 months of continuous data via 32 MB Flash MMC card (64 MB cards are

also available); when full, the wraparound feature replaces oldest data with

most recent data

DUE TO ONGOING RESEARCH AND PRODUCT IMPROVEMENT, SPECIFICATIONS ARE SUBJECT TO CHANGE WITHOUT NOTICE.

RATINGS AND CERTIFICATIONS: 	n Class I, Div. 1, Gr.  A, B, C, D 	ATEX: X g II 1 G

(Intrinsic safety) 	American Bureau of Shipping 	EEx ia IIC

IECEx: Ex ia IIC

BAM: certifi ed for methane measuring function up to the lower explosive

1 	limit in air. BAM certifi ed for oxygen measuring function.

2

1   Smaller: Weighs only   7.4 oz. / 211 g

2   Triple Alarm System: 95 dB audible, dual

alarm bars and internal vibrator alarm

3   Tougher: Equipped with integral concussion-

proof boot for the most rugged environments

5

4   Large, high-contrast LCD shows real-time

gas concentrations for all four gases

simultaneously and continuously

5   Easy, pushbutton operation

4 	Support CD-ROM

6   Flexible power operation

●  Two AA Alkaline cells (16-18 hours typical) or

●  Two NiMH cells (14-16 hours typical)

6

7   Optional datalogger with 32 MB Flash MMC

7 	data storage

Fax: +1-403-273-3708	Locally distributed by:

Email: info@bwtnet.com

www.gasmonitors.com

BW1006-01-01-00-8.25x11-20050624-5359-14